## Slide 1: The Security-Utility Trade-off for Iris Authentication and Eye Animation for Social Virtual Avatars
Brendan David-John
PhD Student
University of Florida
Sanjeev Koppal
Assistant Professor
University of Florida
Eakta Jain
Assistant Professor
University of Florida
Sophie Jörg
Associate Professor
Clemson University
Web: www.jainlab.cise.ufl.edu/Privacy_and_Security_in_Eye_Tracking.html Email: brendanjohn@ufl.edu

## Slide 2: Introduction
hubs.mozilla.com - Hubs by Mozilla

## Slide 3
Video by TECH@Facebook™
“Codec Avatars: Conversation in VR”
https://tech.fb.com/codec-avatars-facebook-reality-labs/

## Slide 4: Threat Model
Untrusted Eye Tracking Platform/System
Adversary wants to steal your password to spoof login
EX: Adversary gains access to data port used by eye camera
The iris biometric is stolen and used to access secure account

## Slide 5: Related Work
Augmented Reality: Malicious inputs/outputs
  [Jana et al., IEEE SP’13 & USENIX’13] , [Lebeck et al., IEEE SP’17 & ’18]
Wearables: Privacy of bystanders
  [Neustaedter et al., ACM TOCHI’06], [Hasan et al., ACM CHI’18]
Eye Tracking: Privacy of the scene camera and gaze datasets
  [Liu et al., ACM ETRA’19 ], [Steil et al., ACM ETRA’19]
Our Prior Work: Secure iris biometric within eye image
  [John et al., ACM ETRA’19]

## Slide 6: Research Problem
How might we transform the eye image to “turn off” the biometric, i.e., to secure iris signature?

## Slide 7: Separable in Frequency Domain
Iris
Pupil
Iris
Glint

## Slide 8: Key Insight: Optical Defocus
Tele-scoping
Arm
Eye Camera
In-Focus Configuration
Increased
Eye Distance
Out-of-Focus Configuration

## Slide 9: Contribution: How much blur?
σ = 0 pixels
Gaze error = 1.4º
CRR = 79%
σ = 3 pixels
Gaze error = 1.9º
CRR = 5%
σ = 8 pixels
Gaze error = N/A
CRR = 0%

## Slide 10: Security-Utility Tradeoff
5% CRR
Security: Iris Recognition
Utility: Gaze Accuracy
Out-of-focus
In-focus

## Slide 11
RQ1 : At what level of blur do viewers notice a difference in the animation of an avatar’s eyes relative to a reference?
[Detection Threshold/PSE]
RQ2 : What is the relationship between level of blur and the avatar’s perceived naturalness, truthfulness, attentiveness?
[Perceived attributes]
Contribution: Perceptual Studies

## Slide 12: Stimuli Generation
Conversational gaze data
Gaze directions transferred to an avatar
Eye images sent through software blur
Gaze directions from blurred images transferred to an avatar

## Slide 13
σ = 5 pixels
Stimuli Generation

## Slide 14
Method: 20 participants shown reference avatar and avatar with eye movements estimated from secure eye images.
Asked “Are they same or different?”
RQ1 : At what level of defocus do viewers notice a difference in the animation of an avatar’s eyes relative to a reference?
PSE
DT
CRR<5%
CRR<2%

## Slide 15
RQ2 : What is the relationship between level of defocus and the avatar’s perceived attributes?
Method: 19 different participants shown one avatar at a time; Asked to provide a rating on a 5-point Likert scale,
e.g., “The avatar was truthful.”
Naturalness
Truthfulness
Attentiveness
Comfort
Eye Contact

## Slide 16
Takeaway: Change in perceived attributes for 𝞂 > 3.
Less than 5% chance of your iris image being usable for identity theft when 3<𝞂<5.
Recommendation: Use a blur kernel with 𝞂<5.
Attentiveness
Truthfulness
What about Social VR?
5% CRR

## Slide 17: Summary
How might we transform the eye image to “turn off” the biometric, i.e., to secure iris signature?
Takeaway 1: Use defocus
Takeaway 2: in software or hardware
Takeaway 3: but select parameters while considering impact on perceived attributes of your avatar

## Slide 18: Limitations and Future Work
This experiment:
  Avatar eyes are the only animated portion
  Perceptual study does not consider the impact of blur on blink detection or pupil diameter estimates
This framework:
  Assumes an eye tracker camera with adjustable focus
  Recommended “sweet spot” in the security-utility tradeoff applies to a fixed iris authentication method
Perceptual Studies
Design Framework
Adversarial Learning

## Slide 19: Thanks!
Please read our paper and visit the website for more details.
Web: www.jainlab.cise.ufl.edu/Privacy_and_Security_in_Eye_Tracking.html
Email: brendanjohn@ufl.edu

## Slide 20: Limitations and Future Work
This experiment:
  Avatar eyes are the only animated portion
  Perceptual study does not consider the impact of blur on blink detection or pupil diameter estimates
This framework:
  Assumes an eye tracker camera with adjustable focus
  Recommended “sweet spot” in the security-utility tradeoff applies to a fixed iris authentication method
Perceptual Studies
Design Framework
Adversarial Learning
[Denis et al., International Journal of Machine Learning and Cybernetics, 2020]
Notes: Our experiment had some limitations, namely only the eyes were animated, which means no blinks, pupil changes, or head movements. To address this in future work we can conduct experiments with more interactive avatars.
Our framework for hardware blur assumes that the user can access the eye tracking camera, however this is not always the case with VR displays. *click* to address this we can consider new optics solutions.
But the one that I am most interested in, is addressing this key limitation of the current work. We have presented a sweet spot for a fixed iris auth method, and we selected this as it is a standard. PPl are coming up with new solutions all of the time, including deep networks,

## Slide 21: Key Insight: Optical Defocus = Low Pass Filter
Telescoping Arm
Eye Camera
In-Focus Configuration
Increased
Lens-eye distance
Out-of-Focus Configuration
Notes: [TODO: Don’t use the VR eye images, use from past slides with an in-focus and out-of-focus even from EyeVeil]
We propose the use of a blur filter to remove the iris signature from the eye image. Blur can be applied in software by convolving with a blur kernel such as Gaussian blur as seen in this video stream. <click> Blur can also be applied in hardware through optical defocus. For this work we add defocus by increasing the distance between the eye camera and the user’s eye. This allows the user to control their own security, and allows them to enable and disable the iris biometric as needed.
Highlight concept of in-focus and out-of-focus configuration